## Slide 1
Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
The 21st International Wireless Communications & Mobile Computing Conference
12–16 May 2025 // Abu Dhabi, UAE
Southeast University
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang
16 May, 2025

## Slide 2
01
Background
04
Simulation Results
02
System Model
05
Conclusion
03
Proposed Codebook Design Scheme
Outline

## Slide 3
Extremely Large-Scale MIMO
XL-MIMO has emerged as a critical technology for future 6G due to its high spatial multiplexing and spectral efficiency [1] .
The transition in electromagnetic propagation characteristics from far-field planar waves to near-field spherical waves also renders traditional beamforming approaches unsuitable[2] .
[2]
[2] M. Cui and L. Dai, “Channel Estimation for Extremely Large-Scale MIMO: Far-Field or Near-Field?” IEEE Transactions on Communications, vol. 70, no. 4, pp. 2663-2677, April 2022.
[1] C.-X. Wang et al., “On the Road to 6G: Visions, Requirements, Key Technologies, and Testbeds,” IEEE Communications Surveys & Tutorials, vol. 25, no. 2, pp. 905-974, Secondquarter 2023.
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
01

## Slide 4
A Narrow-Band XL-MIMO Communication System
Consider a downlink beam training XL-MIMO communication system, the base station with 𝑁antennas communicates with a single-antenna user.
spherical-wave model
Distance：
received signal at UE：
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
02

## Slide 5
Existing Beam Training Schemes
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
Exhaustive Search Based On Polar-Domain Codebook
If given perfect CSI information , the optimal beamforming vector in XL-MIMO can be obtained as .
[1] M. Cui and L. Dai, “Channel Estimation for Extremely Large-Scale MIMO: Far-Field or Near-Field?” IEEE Transactions on Communications, vol. 70, no. 4, pp. 2663-2677, April 2022.
Polar-Domain Codebook[1]
Optimal beamforming vectors from different sampling points
Exhaustive Search: find the optimal codeword to serve as the beamforming vector in the polar-domain codebook that maximizes the received signal power.
Unaffordable Beam training Overhead!
Codebook size:
Codeword
02

## Slide 6
Existing Beam Training Schemes
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
GS-Based Codeword Design For Near-Field 2D Hierarchical Beam Training
[1] Y. Lu, Z. Zhang and L. Dai, “Hierarchical Beam Training for Extremely Large-Scale MIMO: From Far-Field to Near-Field,” IEEE Transactions on Communications, vol. 72, no. 4, pp. 2247-2259, April 2024.
Minimize the discrepancy between the ideal beam pattern and the beam pattern obtained by
The computational cost of calculating the pseudoinverse of matrix during the iteration is rather expensive
Iteratively update two variables [1]
High computational complexity!
[1]
02

## Slide 7
Cluster-Based Hierarchical Near-Field Codebook
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
The proposed CHB scheme seeks to maximize the achievable rate by minimizing the discrepancy between the designed codebook and the polar-domain codebook .
Angle and Distance Clustering
Minimize these cost functions
Angle
Sort both the angular and distance cluster centers are in an ascending order
03

## Slide 8
Cluster-Based Hierarchical Near-Field Codebook
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
Calculation of Beam Codeword Coverage
To construct a multi-resolution hierarchical codebook, angular and distance cluster centers are initially paired to form all possible combinations .
A single angle-distance point
A coverage region in the polar domain
Sort
Angle
Coverage
Codeword
03

## Slide 9
Cluster-Based Hierarchical Near-Field Codebook
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
Hierarchical Near-Field Beam Training
Dynamically adjust the size of each layer's codebook
L layers of sub-codebooks
In–th layer
Coverage
Step Size
Step size is determined by the number of cluster centers:
Significantly reduce beam training overhead
03

## Slide 10
Cluster-Based Hierarchical Near-Field Codebook
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
Overhead and Complexity Comparison
Codeword Design Scheme | Complexity
Near-field 2D hierarchical | 
The proposed near-field CHB | 
Codeword Design Scheme | Complexity
Near-field 2D hierarchical | 
The proposed near-field CHB | 
The proposed CHB scheme achieves approximately two orders of magnitude in codeword design complexity lower than the Near-field 2D hierarchical scheme.
Beam Training Scheme | Overhead
Near-field exhaustive search | 
The proposed near-field CHB | 
Beam Training Scheme | Overhead
Near-field exhaustive search | 
The proposed near-field CHB | 
The proposed CHB scheme significantly reduces training overhead compared with exhaustive search.
The first layer codebook size
03

## Slide 11
Simulation Results: Achievable Rate vs Overhead
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
The proposed CHB scheme achieves a balance between performance and overhead
Beam Training Scheme | Overhead
Near-field exhaustive search | 8192
Near-field 2D hierarchical | 268
The proposed near-field CHB | 227
Parameters | Value
Carrier | 50GHz
Number of antennas | 512
Number of distance girds | 16
15% reduction in overhead than 2D hierarchical
97% reduction in overhead than exhaustive search
Narrow-band
04

## Slide 12
Achievable Rate vs Distance and SNR
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
The proposed CHB scheme achieves suboptimal performance in most cases
Average performance improvement of 10% than 2D hierarchical
Closer to optimal performance
04

## Slide 13
Conclusion
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang: Cluster-Based Low-Complexity Codebook Design for Hierarchical Beam Training in XL-MIMO
Proposed CHB
A cluster-based hierarchical beam-training scheme that applies clustering to polar-domain sampling points, yielding multi-resolution codebooks with minimal design complexity.
Twofold benefits
Codebook design complexity ↓102× — eliminates expensive matrix pseudo-inverses.
Beam training overhead ↓ 97 % — shrinks the search beams from 8192 to 227 while maintaining near-optimal achievable rate.
Future directions:
Extend CHB to wide-band systems; Develop clustering criteria tailored to distributed cell-free XL-MIMO deployments.
05

## Slide 14
THANKS！
The 21st International Wireless Communications & Mobile Computing Conference
12–16 May 2025 // Abu Dhabi, UAE
Southeast University
Jikun Zhu, Xiaochen Ma, Wang Zheng, and Yongming Huang
16 May, 2025