## Slide 1
Matrix-Inversion-Free Expectation Propagation for Massive Connectivity
Rui Ma, Zheng Wang, Yongming Huang
Southeast University, Nanjing, China
Zhen Gao
Beijing Institute of Technology, Beijing, China

## Slide 2
Content
Background & Motivation
01.
System Model & EP Algorithm
02.
Proposed Matrix-Inversion-Free EP Method
03.
Simulation
04.

## Slide 3
IoT-based wireless networks future Internet of Everything (IoE) networks
connect up to a million devices
require massive machine-type communication (mMTC)
Figure 1: Illustration of massive connectivity scenario
massive access
BS: identify active devices
Compressed sensing (CS) framework for sparse signal recovery
Sporadic traffic property
Background

## Slide 4
Proposed method：
Consider EP to incorporate a priori distribution
Existing problems:
Relatively poor performance in current CS algorithms because a priori distribution of the sparse vector is not exploited
Better performance !
Lower complexity !
Estimation accuracy guarantee !
High computational complexity of conventional EP due to repeated inversions of large covariance matrices
Performance loss due to the use of the Hutchinson diagonal estimator
Propose a matrix-inversion-free EP-CG framework that uses preconditioned conjugate gradient (CG) and a Hutchinson diagonal estimator
Theoretically specify the lower bound of probe vectors R in Hutchinson diagonal estimator required to guarantee a desired level of estimation accuracy
Motivation

## Slide 5
System model
Develop a threshold-based approach to sparsify the Gram matrix
pilot matrix
The goal for the BS is to detect the user activities and to estimate the user channels by recovering based on the noisy observation .
likelihood function
prior distribution
Each user transmits its pilot sequence to the BS and the received signal at the BS:
joint user activity and channel information
The optimization problem is computationally intractable due to the discrete nature of the binary activity vector .
MAP estimator:

## Slide 6
EP Algorithm
compute cavity distribution:
moment computation:
moment matching
Construct a tractable approximation of the target posterior distribution:
Iterative EP update rules:

## Slide 7
EP-CG Algorithm
The complexity of the EP algorithm is dominated by the computation of the covariance matrix
matrix multiplication
matrix inversion √ dominant
We propose EP-CG that avoids the direct calculation of
The value of is used in the algorithm in two aspects
the multiplication of to a vector
the diagonal entries of
obtain by solving linear system using CG
estimate full diagonal of by using independent Rademacher probe vectors
use parallel CG to obtain
Hutchinson estimator
matrix multiplication
matrix inversion √ dominant
We propose EP-CG that avoids the direct calculation of
The value of is used in the algorithm in two aspects
the multiplication of to a vector
reformulate this operation

## Slide 8
if the number of probe vectors satisfies
EP-CG Algorithm
Thm 1: For any desired accuracy and confidence level , the estimator’s relative error holds
where
Theoretical accuracy guarantees of the Hutchinson estimator
Complexity Comparison
EP: requires inversion of the full covariance matrix in every iteration. complexity order
Proposed EP-CG: replaces inversion with parallel CG and Hutchinson diagonal estimator. complexity order
EP-CG is significantly cheaper when (easy to satify since in typical massive connectivity regime )

## Slide 9
Simulation
EP-CG closely tracks the superior detection performance of conventional EP as the pilot length increases, with larger yielding steadily better accuracy, while significantly outperforming AMP-MMSE, AMP-soft, and OMP baselines.
EP-CG achieves lower running time than conventional EP across all pilot lengths, delivering an excellent trade-off between detection accuracy and computational efficiency even as varies.

## Slide 10: Thanks for your listening !
Notes: Thank you for your attention. I’d be happy to take any questions.